Drops of LTSpice
Calculate
Heat Dissipation

---
So, you've built an amplifier.
And it is working properly.

---
But how much power is it dissipating?
We already know how to plot this.
The maximum power is 136.21mW.

---
Checking the datasheet and doing some math, the junction temperature is…
TJ = PMAX x Rϴ + TA
TJ = ( 136.21 x 10-3 x 200 ) + 25 = 52.24⁰C
Easy, isn't it?

---
But, couldn't we take advantage of LTSpice to do this for us?
Yes, we can do that!
First, we need understand how to transform thermal dissipation into an electronic circuit.

---
The flow of temperature is like the flow of direct current. So, we can consider this conversion:
And the circuit is simple:
Junction Temperature
Ambient
Temperature
RJC
RCH
RHA

---
The secret to assembling this circuit in LTSpice is the Arbitrary Behavioral Current Source.
It allows you to create a current source numerically equal to the power of the transistor.

---
For our circuit, this is the formula.
As we are using 2N2222 in the TO92 package, we only have one thermal resistance.
Let's use RϴJA, which is the thermal resistance of the Junction to the Ambient.

---
And this is the circuit that simulates the Junction temperature.
Keep in mind that we converted temperature [⁰C] to Volts, so we are interested in the voltage across the junction.

---
As we can see, the circuit agrees with the calculation.
The 52V in TJ is the 52⁰C on the junction.
Francesco Sacco
linkedin.com/in/saccofrancesco