Drops of LTSpice
What is possible to do with the waveform?

---
Let's imagine you have a simple voltage divider.
Note that we use Label Net to name the wires.

---
Running the simulation, we have the waveform of the OUT signal.
The waveform is relative to ground, in other words, the voltage across R2.

---
But what if I want the voltage across R1?
How to measure just this voltage?

---
Measuring V(IN) is not a solution, as the voltage is in relation to ground.
It is the voltage of the source V1, not the voltage of the resistor R1.

---
There are some ways to solve this problem!
First, right-click to open the Expression Editor.

---
You can subtract the voltage
V(IN) and V(OUT).
This is the voltage across R1.

---
You can subtract the voltage
V(IN) and V(OUT).
This is the voltage across R1.

---
LTSpice also allows you to simplify this using V(IN,OUT).
The result is the same.

---
You can measure the current through resistor R1 using I(R1)
Notice that the Y axis has changed to current automatically.

---
It is even possible to calculate the power over R1 using
V(IN,OUT) * I(R1)
And the Y axis now shows the power.

---
It is even possible to calculate the power over R1 using
V(IN,OUT) * I(R1)
And the Y axis now shows the power.

---
Let's imagine that now you have a standard linear regulator.
Its input is 9V and its load R2 is regulated with 5V.

---
You already know that you can measure input and output voltage.

---
But using the right formula, you can present the in/out power.
Note that the source current is negative because of the direction.

---
Calculating correctly, even efficiency becomes easy to visualize.
Francesco Sacco
linkedin.com/in/saccofrancesco