Drops of LTSpice
How to use Operational Amplifiers

---
So... the operational amplifier is a basic component for electronic projects.
And of course LTSpice has a list of options in its library.

---
But there are some differences you need to consider.
Let's start with the basics.
A gain 10 inverting amplifier using an OP07.

---
The result is correct as we expected.
A VIN signal of 100mV generates a VOUT signal ov 1V.

---
Considering an ±8V supply, a 1V VIN signal will saturate the output.
And that is exactly what we can see.
+8V
-8V

---
It also has a current limit on the output, like a real component.

---
So, LTSpice simulates OP07 perfectly, right?
Well… yes and no.
Simulations don't work well outside of boundaries.
Let's imagine that we feed this same circuit with ±50V, even though the limit is ±18V.

---
The simulation remains working, even if the circuit does not represent reality.

---
Now, let's get to know the universal amplifier.
LTSpice has the UniversalOpAmp, a component capable of behaving like an ideal amplifier.

---
Repeating the tests, it behaves exactly as seen before.

---
However, it does not require power to work.

---
The gain seems to have no limits.

---
And… oh boy… you can draw current from it.
Francesco Sacco
linkedin.com/in/saccofrancesco