Drops of LTSpice
How to use Switches?

---
We often need switches in our circuits.
However, sometimes it's annoying to have to deal with calculations and values just for a proof of concept.

---
LTSpice provides a perfect component for this.
The Voltage Controlled Switch.
Let's see how to use it.

---
The switch opens and closes depending on the voltage at the control terminals.
You need to set a directive for your switch.

---
This is the simplest directive.
Note that it has the name we defined for the switch, in SW() with an empty parameter.

---
LTSpice will assume default values.
Name	Description	Default Values
Vt	Threshold voltage	0.0 V
Vh	Hysteresis voltage	0.0 V
Ron	On resistance	1.0 Ω
Roff	Off resistance	1.0 GΩ
Lser	Series inductance	0.0 H
Vser	Series voltage	0.0 V
Ilimit	Current limit	Infinite
In this case, any positive voltage will close the switch.

---
And out tests shows that any positive voltage closes the switch.

---
We can also set a different threshold voltage and resistances by changing the directive parameters.
Now, the threshold is 1V.

---
And you can easily use it instead of a transistor, for example.
Francesco Sacco
linkedin.com/in/saccofrancesco