Drops of LTSpice
How to use the
Arbitrary Voltage Source

---
LTSpice contains a very interesting component...
The
Arbitrary Behavioral Voltage Source

---
It looks like a standard voltage source.
But notice the
V=F(...)

---
By editing the component, it is possible to add a mathematical function
This function will define the voltage behavior.

---
In the software's help window you can get details of all the functions that can be used, searching for Waveform Arithmetic
But I will demonstrate some of them.

---
There are some constants that you can use. The pi, for example.
time is another important keyword!

---
To have a 1kHz sinusoidal signal, the function is
V=sin( 2 * PI * time * 1000 )

---
And to have a cosine…
V=cos( 2 * PI * time * 1000 )

---
LTSpice allows advanced functions
V=sin( 2 * PI * 100 * time ** 2 )

---
Very advanced functions.
Here we use an arbitrary source to calculate the error, and the result is fed to another to perform a PI.
Francesco Sacco
linkedin.com/in/saccofrancesco