Drops of LTSpice
How to do AC Analysis?

---
Let's imagine you've made a transistor amplifier.

---
Of course it works great!

---
But how does it behave at different frequencies?
It's hard to test all the possibilities.

---
But there is a simpler way!
LTSpice analyzes the frequency response for you.

---
First, let's open the advanced properties of your signal source.
Write 1 in the AC Amplitude. This value means 0dB, which will make our analysis simpler.

---
Change the simulation command to AC Analysis. For this circuit, the 10Hz to 100KHz range looks good.

---
The X-axis is typically logarithmic, and 1K per decade is fine.

---
And that's it. Your circuit now displays the frequency response!

---
The solid line is the frequency response. The dotted line is the phase of the signal.

---
Using the STEP directive, you can parse multiple component values.
Here I tested the capacitor between 1uF, 3uF and 5uF.

---
And the result is beautiful!
Francesco Sacco
linkedin.com/in/saccofrancesco